Use Cut & Paste to place the following instructions for installing a smoke detector in correct order.  Renumber the list.

- Make sure you have a drill and a screwdriver.

- If you are installing a Plug-in detector, use a restraining device so that it cannot be unplugged by accident.

- Mount the detector high on a wall or on the ceiling. Wall-mounted units should be mounted so that the top of the detector is 4 to 12 inches (10 to 30 centimeters) from the ceiling. A ceiling-mounted detector should be attached at least 4 inches (10 centimeters) from the nearest wall. In a room with a pitched ceiling, mount the detector at or near the ceiling's highest point.

- Check for proper operation and instructions on its maintenance and operation.

- Check to see if the detector can also be hard-wired into your building's electrical system.

- Make sure that the smoke detector is not connected to a circuit that can be turned off from a wall switch.

- Install, mount and secure your new unit following the manufacturer's instructions.

- If mounting the smoke detector on a stairway with no doors at the top or bottom, position the detector anywhere in the path of smoke moving up the stairs.

- Always position smoke detectors at the bottom of closed stairways, such as those leading from the basement. Dead air trapped near the door at the top of a stairway could prevent smoke from reaching a detector located at the top.

- Disconnect your existing unit.